## Slide 1: The Horizon Simulation Framework
Discussion with Boeing

## Slide 2: Agenda
What is the Horizon Simulation Framework?
Background on Horizon development
Current projects
Appendix

## Slide 3: What problem is HSF trying to solve?
"Systems Engineering Process II" by Leon Osborne, Jeffrey Brummond, Robert Hart, Mohsen (Moe) Zarean Ph.D., P.E, Steven Conger https://commons.wikimedia.org/wiki/File:Systems_Engineering_Process_II.svg#/media/File:Systems_Engineering_Process_II.svg
Verification and Validation of System Level Requirements can be difficult if the system is not operations
Notes: Main system level requirements can best be verified by simulation (Utility or Use Requirements)
Attack the problem by developing a model of the system that, when exercised, will simulate the behavior of the system over time

## Slide 4: What is HSF?
Scheduler/System Interface
Main Scheduling Algorithm
System Parameters (Custom Model File)
Simulation Parameters (Custom Simulation File)
Final Schedule, State Data (Output)
System Model
Subsystem
Subsystem
Subsystem
Horizon Simulation Framework
Interface between Subsystems
Task Inputs
(Custom Task File)
Modeling Utilities
Code Interactions
Input/Output Interfaces
Notes: A library of integrated software tools supporting rapid system-of-systems modeling, simulation and utility analysis
Provides an extensible and well-defined modeling capability concurrent with a scheduling engine to generate operational schedules of Systems-of-Systems with corresponding state data
Modular, Flexible with built-in utilities

## Slide 5: Example of using HSF
A rev-in-the-life of the Aeolus constellation
Aeolus: The Greek ruler of wind
Extreme-weather imaging satellite
Circular, 1000km, 35 degree inclined orbit
Simulation date: August 1st 2008 for 3 revolutions
Targets clustered into high-risk areas, including Southeast Asia and the Gulf of Mexico
Sensor has ability to generate data while in eclipse
Notes:   Aeolus Test Case – Rev. In The Life used to verify a utility based system-level requirement

## Slide 6: The Aeolus Results: Visualization
Matlab visualization of HSF simulation results

## Slide 7: The Aeolus Model
ADCS
Actuates spacecraft to target in user defined slew time
EO Sensor
Takes data in user defined low, medium or high resolution (number of pixels)
SSDR
Records data in user defined storage buffer
COMM
Downlinks data at user defined downlink rate
Power
Maintains depth of discharge information from subsystem power usage and solar panel power in

## Slide 8: v3.0 Targets Hit
307 Hits

## Slide 9: Asset 1 Data

## Slide 10: Asset 1 Data

## Slide 11: Asset 2 Data

## Slide 12: Asset 2 Data

## Slide 13: How Does HSF Work?
Subsystem 1
Subsystem 6
Subsystem 2
Subsystem 3
Subsystem 9
Subsystem 8
Subsystem 10
Subsystem 12
Subsystem 11
Subsystem 7
Subsystem 5
Subsystem 4
Asset 3
Asset 1
Asset 2
Notes: Constraints – a limit on values of a system state variable
Dependency – describes the relationship between one or more subsystems
Asset – a collection of subsystems with some significant meaning to the modeling engineer

## Slide 14: The Scheduler
A
A
B
B
C
C
A
C
B
A
B
t0 t1 t2
A
B
C
C
B
B
t0 t1 t2
The process continues adding 4 more schedules but only 5 more elements in memory.
1.
2.
3.
4.
5.
6.
7.
Reference
C
C

## Slide 15: Progress since Fall 2015

## Slide 16: Two Major Improvements
Redeveloped the architecture of HSF as a series of stand-alone projects using C#
  More maintainable, learnable and usable
  Better support for unit testing
  Uniform Coding Style
  Take advantage of .NET framework and Github source control
Implemented Python scripting support

## Slide 17: One Major Enhancement
Dynamic constraint checking
  The constraint and subsystem checking order can be updated dynamically
Constraint failure feedback
  Information on the cause of each constraint failure is provided to user for design consideration

## Slide 18: Current/Future Work
Optimizing code
  Adding multithreading
  Minimizing memory allocation
Developing MBSE/sysML based model schema
Building additional models for reuse
GUI integration
Unit testing is on going

## Slide 19: Moving Forward
Three current graduate students working on HSF
PloySim club
  Many undergraduates looking for projects
Developing elective course in Modeling and Simulation
We are looking for projects/ideas